## Slide 1
Global Wind Atlas
Global overview with the details
Presented by Jake Badger
Head of Section, Wind Resource Assessment Modelling
Department of Wind Energy
Technical University of Denmark
DTU Wind Energy
A lecture given as part of the course on:
Building Weather and Climate Services for the Energy Sector
18-20 May, Shanghai, China

## Slide 2: Outline
Introduction to DTU Wind Energy
Background and context of the Global Wind Atlas
The Team
The Methodology
The Service: overview
The Service: demonstration
Future developments

## Slide 3
Høvsøre Test Station 2003
Østerild Test Centre 2014
DTU Risø Campus
DTU Lyngby
Introduction to DTU Wind Energy

## Slide 4
DTU Wind Energy
Test and Measurements
Aerodynamic Design
Fluid Mechanics
Material Science & Characterization
Composites & Materials Mechanics
Resource Assessment Modelling
Meteorology and Remote Sensing
Integration and Planning
Loads and Control
Structures and Component Design
Offshore wind energy
Siting and integration
Wind turbine technology
Research based consultancy and tests
Education and teaching
Introduction to DTU Wind Energy

## Slide 5
5
Generalized Wind Climate from NWA
High resolution map
Turbine power curve
WAsP includes option for CFD calculation of flow corrections
DTU Resource Assessment software: WAsP

## Slide 6: DTU Resource Assessment Software on the world map
30 years of development
o More than 5000 users
o More than 250 certified WAsP users
National wind atlases … ■
Regional and local studies … ■
WAsP course venues … ■
Certified users … ■
Methodology global impact

## Slide 7: Background and context of the Global Wind Atlas
Global Wind Atlas
GWA 1.0
2015
23 participating CEM governments account for 80 percent of global greenhouse gas emissions
Lead countries are Denmark, Germany and Spain.+ 11 countries and EC
Coordinated by
International Renewable Energy Agency (IRENA)
Global Wind Atlas by DTU Wind Energy
Funded by
Energy Technology development and Demonstration (EUDP)

## Slide 8: Background and context of the Global Wind Atlas
www.globalwindatlas.info
www.globalsolaratlas.info
www.energydata.info
Next step of Global Wind Atlas (GWA 2.0) 2017

## Slide 9: The Team
DTU Wind Energy
J Badger, B Hansen, N Davis, B Olsen, A Hahmann, N Mortensen, J Hansen
Nazka Mapps
I Bauwens, I Dautashvil, D Codrescu, A Vaidya
World in a Box
        and colleagues
D Heathfield, M Onninen

## Slide 10: The Team
Vortex
O Lacave, P Casso, G Lizcano, A Bosch
World Bank
O Knight, T P Nguyen, S Krohn

## Slide 11: Global Wind Atlas model chain

## Slide 12: Mesoscale modelling
310 WRF mesoscale modelling tiles
Each is 9 x 9 degrees (+buffer)
Resolution is 9km
ERA-Interim reanalysis provides the boundary conditions
Sampled from period 1997-2016

## Slide 13: ERA-Interim reanalysis at ~70 km resolution
Reanalysis ECMWF ERA-Interim 1997-2016 average wind speed at 100 m a.s.l.
Resolution not high enough

## Slide 14: Mesoscale downscaling at 9 km resolution
Vortex WRF Downscaling driven by ERA-Interim 1997-2016 average wind speed at 100 m a.s.l.
Resolution not high enough

## Slide 15: The need for downscaling
Mesoscale modelling
Microscale modelling

## Slide 16: The need for downscaling

## Slide 17: Global Wind Atlas model chain Generalization
Each mesoscale model grid point climate is generalized
The purpose of generalization
  to express wind climate in a standardized way
  to remove the impacts of the mesoscale topography on the local winds
  To prepare input for microscale modelling
Result: wind climate for flat terrain with uniform roughness

## Slide 18: Global Wind Atlas model chain Generalization
Mesoscale modelling performed on overlaping domains on native modelling grids
Generalized wind climate regridded to regular longitude latutide grid
Slight difference in wind climate at mesoscale boundaries
Interpolation performed between domains
After
Before

## Slide 19: Global Wind Atlas model chain microscale modelling
2439 jobs required to cover land and 30 km offshore
Calculation system runs WAsP-like microscale modelling over vast areas using many computer nodes.
It manages and despatches inputs
  Generalized reanalysis winds
  High resolution elevation and surface roughness data
First pass, sample spacing is 1 km
Second pass, sample spacing 250 m

## Slide 20: Microscale Orographic speed-up
Modification of the wind profile
Winds speed up on hills
Winds slow down in valleys
Handled by WAsP modelling

## Slide 21: Microscale Surface roughness length
Handled by WAsP modelling

## Slide 22: Microscale Surface roughness length
New log-profile
Transition profile
Unchanged profile
Rule of thumb: 1:100
Handled by WAsP modelling

## Slide 23: Datasets terrain: elevation and roughness
Elevation
Viewfinder, compiles SRTM and other datasets resolution 90 - 30 m, remapped on 150 m grid
Land cover
ESA GlobCover resolution 300 m
Modis, land cover classification resolution 500 m, for gap filling.

## Slide 24: A tour of the website
The website has been completely reinvented
More user friendly
More intuitive and interactive
Search and navigation functions
Simplified
Fewer and most relevant layers remain
Many of the same analysis tools remain
Download possibilities
Documentation

## Slide 25: Launch of Global Wind Atlas 2.0 at WindEurope
  High Profile
  Ranjit Lamech, Director at World Bank’s Energy & Extractives
  Jens-Otto Horslund, Ambassador of Denmark to the Netherlands
  Laurent Humbert, Engineering Manager at EREN Groupe
  globalwindatlas.info

## Slide 35
10 % windiest area
power density at 100m
650 W/m2

## Slide 36
10 % windiest area
power density at 100m
542W/m2

## Slide 37
10 % windiest area
power density at 100m
773 W/m2

## Slide 38: Exploring an interesting area in Chad with the GWA
An area with power density in excess of 800 W/m2 at 100 m a.s.l.

## Slide 39: Exploring an interesting area in Chad with the GWA
An area with power density in excess of 800 W/m2 at 100 m a.s.l.
The area is near the city of Fayo Largeau
The area is in Borkou region

## Slide 40: Exploring an interesting area in Chad with the GWA
An area with power density in excess of 800 W/m2 at 100 m a.s.l.
The area is near the city of Fayo Largeau
The area is in Borkou region
Wind speeds in the area in excess of 8 m/s at 100 m a.s.l.

## Slide 41: Exploring an interesting area in Chad with the GWA
An area with power density in excess of 800 W/m2 at 100 m a.s.l.
The area is near the city of Fayo Largeau
The area is in Borkou region
Wind speeds in the area in excess of 8 m/s at 100 m a.s.l.
It appears to be a desert region in contrast to the southern regions of Chad

## Slide 42: Exploring an interesting area in Chad with the GWA
An area with power density in excess of 800 W/m2 at 100 m a.s.l.
The area is near the city of Fayo Largeau
The area is in Borkou region
Wind speeds in the area in excess of 8 m/s at 100 m a.s.l.
It appears to be a desert region in contrast to the southern regions of Chad
The roughness length is very low

## Slide 43: Exploring an interesting area in Chad with the GWA
An area with power density in excess of 800 W/m2 at 100 m a.s.l.
The area is near the city of Fayo Largeau
The area is in Borkou region
Wind speeds in the area in excess of 8 m/s at 100 m a.s.l.
It appears to be a desert region in contrast to the southern regions of Chad
The roughness length is very low
There is an orographic gap feature

## Slide 44
10 % windiest area
power density at 100m
1042W/m2

## Slide 45
10 % windiest area
power density at 100m
1718 W/m2

## Slide 47: Validation at sites
Mesoscale modelling
C1, check model derived generalized wind climates: test of mesoscale modelling and generalization
ref: measurement derived generalized wind climate
C2, check predicted wind climate using model derived generalized wind climate and best site topography
ref: measured wind climate
C3, check global wind atlas (nearest point): test of global topography + displacement of site effect
ref: predicted wind climate using model derived generalized wind climate and best site topography
C4, check global wind atlas (nearest point): test of complete model chain and + displacement of site effect
ref: measured wind climate

## Slide 48: Validation
C2, check predicted wind climate using model derived generalized wind climate and best site topography
ref: measured wind climate
44 Sites
Mean error: -6% Mean absolute error: 10%

## Slide 49: Validation
ESMAP measurement campaigns
High quality wind measurements
Site survey and microscale modelling
Plus our measurement datasets

## Slide 50: Future perspectives for GWA 2.0, GWA 3.0, and beyond
Over all aim is to making GWA
  more accurate
  more relevant
  more valuable
How?
  Validation and new model chain
    Quantify and characterize uncertainty
    Flow in complex terrain and stability effects
    Roughness length evaluation
  New Layers
    Design parameters: extreme wind load conditions EOG, EWS, ECD, EDC and ETM
    Capacity factor for custom power curves
    Cost modelling
Validation and research are interlinked
The GWA is DTU Wind Energy’s
as launch pad for new wind energy datasets to increase impact

## Slide 51: www.globalwindatlas.info
GWA2.0 in first 169 days has attracted
>54920 sessions
>31492 users
in 201 countries
Approximately:
250 sessions per day
150 users per day
THANK YOU FOR YOUR ATTENTION

## Slide 53: Globcover classes to Roughness length (m)

## Slide 55
10 % windiest area
power density at 100m
650 W/m2

## Slide 56
10 % windiest area
power density at 100m
542W/m2