## Slide 1
Carlo Buontempo
With contributions from: Jean-Noël Thepaut, Dick Dee,
Anca Brookshaw, Cedric Bergeron, Eduardo Penabad Ramos
ECMWF
@carlo_tuitter ; Carlo.Buontempo@ecmwf.int
Notes: Hello, I am Carlo Buontempo
I am a physicist by training, I have worked on climate change adaptation and cliamter services for the best part of the last 10 years. Now I lead something called the Sectoral Information System of Copernicus Climate Change Service.
Effectively I am here today to tell you all you have always wanted know about Copernicus Climate Change Service but never dared asking.
But before I do that let me ask YOU some questions:…

## Slide 2
z
Notes: Well, Copernicus is an ambitious remote sensing project funded by the European Commission. This means that most of its effort is directed toward the design, testing, launching and management of satellite sensors and platforms. But alongside the SPACE component the program also has a service component structured around six thematic areas: atmosphere, marine, land, emergency, security and climate change.
The European Commission has entrusted ECMWF, the European Centre for Medium Range Weather predictions I here represent, to manage and run two of these services: Atmosphere and Climate Change.

## Slide 3
Climate Data Store – CDS
The CDS contains observations, global and regional climate reanalyses, global and regional climate projections and seasonal forecasts.
The CDS is designed as a distributed system, providing improved access to existing datasets through a unified web interface
Notes: Essential Climate Variables. An ECV is a physical, chemical or biological variable or a group of linked variables that critically contributes to the characterization of Earth' s climate.
3

## Slide 4: Climate projections
Service: Providing users with timely access to climate change scenarios produced with state-of-the-art climate models (CMIP, CORDEX)
Notes: Going even further away from the satellite observations C3S also provide access to climate projections both at a regional and global level. In this case satellite information doesn’t play any role in initializing the simulations but it can be used instead as a away to validate the model performance in present-day climate.

## Slide 5: OLD weather
Courtesy of Philip Brohan @PhilipBrohan

## Slide 6: C3S data rescue
Registry services for data rescue projects
Improved access to detailed metadata for active projects
Tools and best practices, capacity building
Support for selected high-priority data rescue activities

## Slide 7: Observations from global climate data archives
Merge of major land and marine surface data collections
Data quality control and homogenisation
Harmonisation of data and metadata under a Common Data Model
Unified data access via the Climate Data Store

## Slide 8: Essential Climate Variables
Notes: The point here is just to say that there are many variables and we will ultimately give access to as much of them as possible

## Slide 9: High-resolution ECV products for Europe
Temperature, precipitation, humidity, wind (Building on ECA&D and E-OBS)
Data collection, quality control and homogenisation
Gridded ECV datasets and climate indices

## Slide 10: Climate reanalysis: ERA5
Atmosphere/land/wave parameters
31 km global resolution, 137 levels
Hourly output from 1979 onward
Using 2016 ECMWF forecast system
Using improved input observations
Ensemble data assimilation method
Uncertainty estimates for all ECVs
Notes: Another way of using satellite data is to ingest them into a NWP model. This is what is routinely done in weather predictions. The retrospective re-run of the weather prediction model with all the available data is known as re-analysis. C3S is producing a new high-resolution coupled global reanalysis known as ERA50.
There are several new features of these new reanalysis including a NRT update and a assessment of the observational uncertainty.

## Slide 11: C3S seasonal forecasts - Introduction
Aim: to generate seasonal forecast products based on the best information available, to an operational schedule, and make them publicly available.
Horizontal grid: global 1deg x 1deg
Ensemble size:
  Forecasts: ~50 members
  Hindcasts: ~25 members x 24 years (1993-2016)
Variables
  Surface
    7 vars every 6h
    +30 vars every 24h
  Pressure (11 levels, from 925 hPa to 10 hPa)
    8 vars every 12 h
Agreed NetCDF specification C3S-0.1 (based on CF)
Notes: Moving away from reanalysis, satellite data is also useful to initialise climate prediction models. C3S provide free and unrestricted access to 3 and soon 5 seasonal prediction model. This are coupled models designed to provide indications of the future evolution of the atmosphere and the oceans over a period of a few months.
5 contributors
Current: ECMWF, MeteoFrance, Met Office
Soon (May/June?): DWD, CMCC, update MeteoFrance to system6
Non-European partners:
NCEP (NOAA), JMA: end of 2018?. Terms under negotiation
Also likely BoM, ECCC, but negotiation not yet started

## Slide 12
Climate Data Store
Searching and Browsing Functions
Notes: Catalogue navigation
Interactive download
API download
Toolbox applications for datasets
Toolbox Gaia-Studio v1.0
12

## Slide 13
Climate Data Store
Discovery
and Retrieve Functions
Gridded Satellite Observation Example
+ APIs

## Slide 14
Climate Data Store
User Requests and Download Functions

## Slide 15
Climate Data Store - implementation
Ongoing physical implementation:
  On-Premises Private Cloud :
    CloudFerro
      34 compute servers x 2 cpu x 12 cores@ 2.2 GHz and 192 GB RAM per server
      4 compute server x 2 CPUs x 8 cores @ 2.6 Ghz and 64 GB RAM per server
      100 TB SSD and 900 TB HDD
Phase I

## Slide 16
Climate Data Store - Toolbox
Toolbox:
The CDS provides an authoritative set of software that will allow users to develop applications that will make use of the content of the CDS
Notes: Technical challenges:
  Diversity of users
  Diversity of data sets
  Very large data volumes
  Data residing at different locations
  Interoperability, efficiency
  User-defined workflows
  Variety of presentation methods
  Need for interactivity
  Access via API
  User management
  Performance monitoring
16

## Slide 17
Climate Data Store- Toolbox
Notes: 17

## Slide 18: Climate data store
to provide practical examples of how C3S in general and CDS in particular could deliver information of relevance to specific sectors.
To act as benchmarks of good practice.
To document users needs, and whenever possible address those.
In particular SIS contract should develop and make available
sector-relevant indicators and tools that were either unavailable or inaccessible before.
Notes: Copernicus is a large European programme of earth’s observation. It is mainly designed to launch and manage a new generation of satellites called the sentinels but alongside the so-called space component the programme has also defined 6 services designed to make satellite information usable to address some of the main challenges our society faces. Two of those services –namely CAMS and C3S- have been given to ECMWF to run.
One of the main features of C3S proposition is the so called Climate Data Store. This is – contrary to its name- neither a shop –as nothing is sold there- nor a storage unit. It is rather a standardized access point to a huge wealth of data related to climate. The key idea of the CDS is to make as much of the post-processing close to the data so that kb of information can be passed to the users rather than terabytes of raw data.

## Slide 19: Data is not information without users and context: co-design in practice …
This is a small subset of the set of users SMHI have engaged with in one of our SIS contracts. We had so far 17 of those contracts.
It is difficult to summarise all we learnt but:
Many users just want data: good data, easy to access and well characterised.
Our primary users are not necessarily the end-user but rather the intermediate ones
Italy
Spain
Netherlands
Sweden
Slovakia
Sweden

## Slide 20
Stakeholder Engagement: Workshops

## Slide 21
Contract led by Uni. Reading
Already ˜1400 entries !

## Slide 22: swicca.climate.copernicus.eu
Contract led by SMHI
Pechlivanidis et al EGU2018-5194

## Slide 23: Water resources and drought
Using a combination of chain of models linking future climate scenarios with hydrological parameters it has been possible to produce an operational assessment of current and future conditions. The water-agriculture-energy nexus provide a good example of how climate mitigation and adaptation can be intertwined. Madrid, in the small plot faces significantly different hydrological futures depending on the mitigation strategy adopted.
Samaniego et al. Nature Climate Change volume 8, pages421–426 (2018)
doi:10.1038/s41558-018-0138-5

## Slide 24: Ex-post bias evaluation: what can the impact modelling tell us about the model biases?
Notes: This slides shows the cumulative losses due to wind-storm for each nation and year in the record. These estimates were obtained downscaling reanalysis data at 4km, analysis the 2s wind gust and then mashing up this filed with the information about the position of the buildings, their nature and the local GDP. As it is possible to see the UK is the most exposed nation in Europe followed by Germany and Jan 1990 looks as the most expensive year. Following this approach which was put together by CGI
Now, the same operation can be repeated for each windstorm in the catalogue and make the sums. This highlights, for example, the fact that the UK is the most vulnerable to wind-storm losses and that the most costly month was Jan 1990.This approach also allows us to see the geographical distribution of the losses at a sub-national level.

## Slide 25: Monthly forecasts for hydro power in France
Increasing share of power supply from variable renewable energy (RE) sources. Demand variability is also increasing. The transformation is taking place against a variable and changing climate.

## Slide 26
Stakeholder Engagement: Workshops

## Slide 27: Energy projections
Integrating climate and energy scenarios to learn how well prepared our infrastructure is to cope with the climate of the future. Will the renewable dominated energy mix of the future able to cope with the expected change in the energy demand profile?
Using a combination of historical data, reanalysis, seasonal predictions and climate projections the SIS contracts demonstrated how will be possible to address some of these questions through the CDS.
Contract led by A. Troccoli UEA
Notes: Climate projections can be used to estimate the value of future solar production in any EU countries.

## Slide 28
Historical monthly generation
Statistical models: no big differences between different models (MLR, SVR, GAM, CARTs …)  ideal for monthly time scales @ country level
Where no data is available for testing, need to use physical models
Monthly hydropower production in Norway
Monthly solar generation in Germany

## Slide 29
Demand modelling – Historical (2)
 | Training | Assessment
RMSE | 36761 MWh | 40194 MWh
MAPE | 2.1% | 2.2%
France

## Slide 30: Seasonal Forecasts (Wind power)

## Slide 31: Data per country for 10 climate models

## Slide 32: PROGRESSES SO FAR
A climate-projection data set suited to the energy sector
  High-resolution 3-hourly, 12 km, 11 models, 2 scenarios, bias adjustment and model selection recommendations
https://esgf-node.ipsl.upmc.fr/search/c3s-energy/
All the data will ultimately become available through the CDS
Proof of concept visualization tools to access data
http://clim4energy.climate.copernicus.eu/
http://ecem.climate.copernicus.eu/demonstrator/

## Slide 33: Operational energy
Building on these proof of concept projects we are now developing an operational service
C3S Energy will cover all time scales (historical, seasonal and multi-decadal)
C3S Energy will provide a series of high-quality datasets that could be used as benchmark
C3S Energy will also provide a set of workflows that will allow anyone to scrutinize and reproduce what has been done.

## Slide 34
climate.copernicus.eu
Carlo.Buontempo@ecmwf.int
@carlo_tuitter

## Slide 36: SIS contracts
The past (2016-2018):
  Energy (UEA, CEA), Water (CEH,SMHI), Insurance (CGI), cities (SMHI), agriculture (TelespazioVega)
The present (2018-2019,..):
  European: storm-surges (Deltares), fisheries (PML), tourism (TEC), cities/health (Vito)
  Global: shipping (OSM), global impacts (SMHI), agriculture (WEnR)
The future :
  in negotiation: energy, water, insurance
  quality assurance for SIS, biodiversity, forestry, cultural heritage, case studies, transport, …
Proof of concept
Operational phase

## Slide 37: What do we mean by Data?

## Slide 38: C3S operational production of global ECV products
C3S tendered activities: 22 ECVs, 5 contracts
In 2018: from 12 to 22 ECVs
Consolidation in 5 contracts
Annual budget ~5 Meuro
Strong heritage in CCI teams
Convergence on data standards
Consistent documentation
Need better quality assurance
White paper on CCI-C3S coordination and roadmap ready by August 2018

## Slide 39: Observations from Baseline and Reference Networks
Focus on atmospheric data: Temperature,
humidity, ozone, wind, CO, CO2, CH4
Data quality control and homogenisation
Harmonisation of data and metadata under a Common Data Model
Unified data access via the Climate Data Store