## Slide 1
Lessons Learned from the Shorter Ranges: Weather Forecasting
for Energy Applications
Dr. Sue Ellen Haupt
Research Applications Laboratory
National Center for Atmospheric Research, Boulder, CO USA
Director of Education, WEMC
Shanghai, China May 19, 2018
Building Weather & Climate Services for the Energy Sector
World Energy & Meteorology Council

## Slide 2: Outline
Examples:
Solar Power Forecasting
Wind Power Forecasting
Hydro Power Forecasting
Theme: Smartly blending data, dynamics, physics, and statistical learning methods
Stakeholder Needs
Ingredients
Forecasting Across Scales
  Numerical Weather Prediction
  Data Assimilation
  Nowcasting (Minutes to Hours)
  Blending
  Power Conversion
  Uncertainty Quantification
  Extreme Events
Assessment
Valuation

## Slide 3: It Takes a Community
Funding Organization
End User
Basic Research Community
Applied
Research Community
Operations
Monitoring
Operations
Computing
Operations
Translation
Partnership:
Public
Private
Academic
Notes: It takes a community working together to accomplish this process effectively.
First the team must understand the needs of the end user.
The basic and applied research community can then build tools.
Public and private entities provide operational monitoring and computing.
It is important to translate the forecasts into usable information based on in depth knowledge of the problem and working closely with the end users.
This process requires collaboration across the sectors – private, public, and academic
[click in individual players]
The SunCast project has striven to bring these communities together as seen in the plethora of collaborators on this project.
The full rainbow cannot be accomplished in any one organization

## Slide 4: Industry Needs for Renewable Energy Forecasts
Need to predict POWER based on met variables
  80-m wind speed
  Surface irradiance – GHI, DNI, DIF
Time frames for prediction
  Long range – weeks –
  maintenance and distribution
  Medium range – days – hourly
  day ahead trading
  Nowcast range – hours – 15-min
  grid integration
  Very short range – seconds to minutes –
  voltage control

## Slide 5: Industry Needs for Renewable Energy Forecasts
Need to predict POWER based on met variables
  80-m wind speed
  Surface irradiance – GHI, DNI, DIF
Time frames for prediction
  Long range – weeks –
  maintenance and distribution
  Medium range – days – hourly
  day ahead trading
  Nowcast range – hours – 15-min
  grid integration
  Very short range – seconds to minutes –
  voltage control

## Slide 6: Value Chain: What is the value of solar power forecasting?
Weather
Monitoring Observation
Modelling
Forecasting
Dissemination & Communication
Uses / Decision Making
Perception Interpretation
Outcomes
Economic & social values
Clouds
Aerosols
Clear Sky
SURFRAD
Satellites
Total Sky Imagers
Pyranometers
WRF-Solar
HRRR
StatCast
TSICast
CIRACast
MADCast
DICast
NowCast
$$
Production Cost Changes
Unit Allocations
Area Forecast
Point Forecast
Reserve Estimates
Reserve Analysis
Projected Power Production
Day Ahead Planning
Real Time Operation
Actual Power Production
Load Balancing
Uncertainty Quant
Power Conversion
Inspired by Jeffrey Lazo

## Slide 7: Meteorological Prediction:
Adapted from Ravela, 2008
Auligne, 2014
= Physical approach

## Slide 8
Meeting the Needs:
Seamless Approach to Solar Power Forecasting
48

## Slide 9: Forecasting System

## Slide 10: Atmospheric Modeling Numerical Weather Prediction
Dynamics
Physics
Quality Assurance
Sensitivity to Initial Conditions
Preprocessing – Needs for Assimilation
Postprocessing – Blending Information
Validation

## Slide 11: Dynamic Meteorology
Numerical methods treat this as an initial value problem
  Discretize in space
  Integrate in time
  Constrained by continuity
  Related by state eqn
Nonlinearities make it difficult

## Slide 12: Quality Assurance in Atmospheric Modeling
Thomas T. Warner
Bulletin of the American Meteorological Society

## Slide 13: Physical Parameterizations
Various processes that we can’t resolve
Thus, parameterize given
  Knowledge of physical process
  Empirics
  Constants and tuning
AJ Deng, Dave Stauffer

## Slide 14: WRF (Weather Research & Forecasting) Model Physics
Turbulence/Diffusion (diff_opt, km_opt)
Radiation
  Longwave (ra_lw_physics)
  Shortwave (ra_sw_physics)
Surface
  Surface layer (sf_sfclay_physics)
  Land/water surface (sf_surface_physics)
PBL (bl_physics)
Cumulus parameterization (cu_physics)
Microphysics (mp_physics)
http://www.google.fr/url?sa=t&rct=j&q=&esrc=s&source=web&cd=2&ved=0CDcQFjAB&url=http%3A%2F%2Fwww.mmm.ucar.edu%2Fpeople%2Fdudhia%2Ffiles%2Fpresentations%2FWRF_Physics_Dudhia.ppt&ei=mKjQUa3qJa6w4QSdnoDgCw&usg=AFQjCNGb933vSVDkzHeeDRk-swIMEZdMrQ&bvm=bv.48572450,d.bGE

## Slide 15: Different Schemes, Different Results
Figure 4. Average rainfall rate, for a spring-season convective event (a), based on
observations (OBS) and for five simulations that used different treatments for the convection -
four different parameterizations, and no parameterization (EX). Also depicted is the rainfallrate
bias score averaged for three warm-season convective events (b), again for each of the
four parameterizations and for the use of no parameterization. The four convective
parameterizations were the Grell (GR), Kain-Fritsch (KF), Betts-Miller (BM), and Anthes-
Kuo (AK) schemes. Adapted from Wang and Seaman (1997).

## Slide 16: Opportunities for prediction
hydrological predictability
meteorological predictability
Water Cycle (from NASA)
Hydrological predictability:
How well can we estimate the amount of water stored in the snow and soil?
Meteorological predictability:
How well can we forecast the weather?

## Slide 17: Value of high-resolution regional model
Resolution : 2.4 km
Notes: Added value of simulation performed with high-res. regional model can be illustrated in this animation.
This animation shows how model terrain gets smoothed out with increasing grid spacing.
Running high resolution model over complex terrain is very important because:
It can resolve vertical motions tied to complex terrain and thus able to produce “close to observed” precipitation pattern.
Having accurate spatial distribution of precipitation is important for properly representing hydrologic balance.

## Slide 18: Snowpack in Central Rockies: too little at high elevation and melts three months too early at coarse resolution
36 km
2 km
April 15 snapshot of snow pack at two model resolutions
(Simulation of 2007-2008 water year)
Notes: Showing snow water equivalent from December 1, 2007 at 36 km and 2km resolutions. The 36 km resolution is similar to resolutions of global climate models. 36 km resolution WRF simulation over water year shows complete loss of snowpack by April 1 and the smearing of snowpack across topographic gradients while 2 km simulation shows snowpack to last through the end of July and also produces the correct spatial pattern as compared to the 111 SNOTEL sites (black dots).
Snow is much less at high elevations and some places that topography is overly smoothed over at 36 km compared with 2km resolution.
Complete loss of snowpack in the 36 km simulation by the end of April, while 2 km has snow lasting through the end of July.
This has a significant impact on runoff seasonality and available water for the drier season when simulating future climate.
The snowpack continues to accumulation in the spring for the 2 km simulation whilethe 36 km model is melting the snow.
Location of snow accumulation also is an important factor to simulate correctly, as southern facing hills melt snow more efficiently, and so on.

## Slide 19
NHDPlusV2-Encompassing Domain
1km NoahMP land model:
  USGS-NLCD land cover (2011)
  NRCS STATSGO, 1km soils
  Climatological vegetation structure (v1.0)
250m routing
  Diffusive wave overland flow
  Saturated subsurface flow
  NHDPlusv2 catchment-based baseflow parameterization
NHDPlusv2 channel routing
  Muskingum-Cunge
  oCONUS manual reach processing….
  2.7M river reaches
  1260 passive, level-pool reservoirs
National Water Model v1.0 Physics Configuration
Model Setup:
Any Questions: gochis@ucar.edu
David Gochis

## Slide 20
Seamless Simulation of Nation’s Hydrologic System
Animation created by:
F. Salas, NOAA/NWC

## Slide 21: Application of Forecasting: Solar Power
Sun4Cast

## Slide 22: WRF-Solar CLOUD-RADIATION-AEROSOL INTERACTION
% Improvement over standard WRF
Courtesy: Pedro Jimenez

## Slide 23: Assimilation provides best ICs
Data Assimilation – incorporating observations into a model
  Surface observations
  Satellite observations
  Atmospheric profiles
  Radar observations
  Data from wind or solar farms
  Specialized data

## Slide 24
Application: Wind Energy Ramping
Real Time Four Dimensional Data Assimilation
RTFDDA
W/O
Farm DATA
With
Farm DATA
Gain:
17 % in RMS
20% in MAE
11% in Bias
0-3 hour Wind Energy Predictions
Courtesy: Yubao Liu

## Slide 25
WRF- RTFDDA Improves
Short Term Forecasts (0-9h)
Courtesy: Tara Jensen, Yubao Liu

## Slide 26
800 MW increase then decrease over 4 hrs!
Time (LST)
Power (MW)
Passing Thunderstorms
Cold Front
Rational for Nowcating:
Wind Energy Ramp Event

## Slide 27
Application: Wind Energy Ramping
Variational Doppler Radar Analysis System
NCAR Auto-Nowcasting System
Gust fronts
approaching
‘wind plant’
Wind ramp
event is
imminent
Wind Farm
Need to provide time-of-arrival and magnitude of wind energy ramp.
Courtesy: Jenny Sun
VDRAS

## Slide 28: Wind Energy Ramp Event Nowcasting
VDRAS
Variational Doppler Radar Analysis System
+
Expert System (obs-based)
Courtesy: Jenny Sun
Notes: To integrate wind energy into the grid on a short term basis requires accurate prediction of wind ramps, which are rapid changes in wind power. To do this, NCAR leverages the Variational Doppler Radar Analysis System (VDRAS), which uses four-dimensional variational (4DVar) assimilation techniques to blend Doppler radar data into a cloud-scale model to provide a physically balanced current state of the atmosphere. An observation-based expert system for nowcasting wind energy ramps has also been developed and is being blended with VDRAS output

## Slide 29: Nowcast System for Solar Power
Nowcast Integrator
StatCast
WRF-Solar
MADCast
TSICast
CIRACast
Irradiance Calculation (POA)
Obs
(Irradiance)
MAD-WRF

## Slide 30: Some Models Employ AI: StatCast
Tyler McCandless

## Slide 31: Sky Imager Forecast
θ1
θ2
6/19/12
Brookhaven NL

## Slide 32: Satellite-Based Forecasting CIRACast - Attention to Details
X
Imagine we are viewing this cloud from the satellite
PV Array
Without account for sensor/sun geometry, the placement of cloud shadows can be 10’s of km in error
Speed Directional Both
TYPES OF WIND SHEAR
Advection of complex cloud layers requires proper account for wind shear
Matt Rogers & Steve Miller: Colorado State University

## Slide 33: MADCast Multi-sensor Advective Diffusive foreCast
AIRS
IASI
MODIS
GOES Sounder
GOES Imager
Multi-sensor
Tom Auligne; Xu et al. (Adv. in Atmos. Sci. 2014)

## Slide 34: Quantify Value - Metrics
 | Model-Model Comparison | Economic Value
Base | Mean Absolute Error Root Mean Square Error Distribution (Statistical Moments and Quantiles) Categorical Statistics for Events | Operating Reserves Analysis Production Cost
Enhanced | Maximum Absolute Error Pearson's Correlation Coefficient Kolmogorov-Smirnov Integral Statistical Tests for Mean and Variance OVER Metric Renyi Entropy Brier Score incl. decomposition for probability forecasts Receiver Operating Characteristic (ROC) Curve Calibration Diagram Probability Interval Evaluation Frequency of Superior Performance Performance Diagram for Events Taylor Diagram for Errors | Cost of Ramp Forecasting
Tara Jensen

## Slide 35: NowCast Performance
CIRACast
MADCast
MAD_WRF
NowCast
SmartP
Statcast_cubist
WRFSolarNow
Aggregated over All Issue times and All Sky Conditions
Component performance varies by lead time
All Compontents have lower MAE (greater skill) after 30 minutes into forecast (lead time)

## Slide 36: SunCast Performance – Day Ahead
SunCast Irradiance
WRFSolar
NAM, GEM, GFS
Day Ahead (DA)
SunCast and WRFSolar
Outperform Baseline (NAM)
and other components

## Slide 37
WRF RTFDDA
HRRR
RAP
GFS
GEM
Other Model Data
.
.
.
Integrator
Wind Power Forecast
Nacelle Winds
Turbine Power Prediction
ECMWF
Wind speed example
10-15% improvement
over best model
Bill Myers
Dynamic Integrated Forecast System (DICast)

## Slide 38
Customized Power
Conversion Curves
Gerry Wiener
Observation-based power curves represent the site better than manufacturers’ power curves
Notes: 38

## Slide 39: Power Conversion
Pattern depends heavily on time of day, AM takes higher route; PM more linear route
Empirical Power Conversion: Regression Tree - Cubist
Example for single axis tracking PV plant

## Slide 40
DICast System Blends Output from Several Numerical Weather Prediction Models
Public Service of Southwestern Public Service Company
Total Power, 03/08 Ramp
CAPACITY (%)
TIME

## Slide 41: Probabilistic Prediction
Recent emphasis in popular scientific literature to emphasize probabilistic approach
Nate Silver thinks meteorologists are ahead of the rest:
  Embrace uncertainty
  Quantify it
  This produces better deterministic forecasts as well

## Slide 42
Fluid Flow is Sensitive to
Initial Conditions
Atmospheric flows display sensitivity to initial & boundary conditions and to physics parameterization
Chaotic Attractor
How do we stay on the correct trajectory?
Assimilation Uncertainty Quantification
Lorenz (1963)

## Slide 43
Ensemble Prediction

## Slide 44: What if we had only one member? Analog Prediction
Binned-spread/skill plot of power predictions from the calibrated ECMWF EPS (red), calibrated COSMO LEPS (blue) and AnEn (black)
Analog Ensemble Method
Statistical learning method to calibrate model output and provide probabilistic information
Based on observed past model-observation pairs
Algorithm search for analogs and clusters them
Shown to perform at least as well as full NWP ensemble systems
Luca Delle Monache & Stefano Allasandrini
Notes: The AnEn method has been applied to a nine 850-kW turbines wind farm located in a region with complex topography in Sicily, southern Italy, to produce an ensemble of power forecasts for the 01/2012-10/2012 period (training data set: 11/2010-12/2011). The AnEn was based on 4-km 78-h predictions from the meteorological model Regional Atmospheric Modeling System (RAMS), with initial and 6-hourly boundary conditions provided by the European Centre for Medium-Range Weather Forecasts (ECMWF) analysis and forecasts, respectively. The performance of the AnEn method has been compared with two advanced NWP-based ensemble forecasting systems, the ECMWF Ensemble Prediction System (EPS) and the COnsortium for Small-scale Modelling (COSMO) Limited-area Ensemble Prediction System (LEPS). Both ECMWF EPS and COSMO LEPS hub-height winds are calibrated with a neural network algorithm (for the first moment) and a variance deficit correction procedure (for the second moment). The ECMWF EPS and COSMO LEPS calibrated wind predictions are then converted to power via the turbine manufacturer power curve. A summary of this comparison is illustrated, which shows the root-mean-square-error (RMSE) of the ensemble means (Fig 1a) as a proxy of ensemble skill, and the binned-spread/skill plot to assess the spread-skill relationship of the analyzed ensembles (Fig 1b).
The AnEn method outperforms the other two advanced systems in this case, exhibiting a 10% (or more) RMSE reduction. Particularly interesting is the better spread/skill correlation of AnEn (being closer to the 1-to-1 line), which equates to better uncertainty quantification and possibly better decision making if those forecast were to be used for real-time operations.

## Slide 45
Normalized Power
Probabilistic Power Prediction
With Analog Ensemble Method
Normalized Power (Nameplate Capacity)
Forecast Lead Time
* Deterministic forecast
* Observations
Percentiles

## Slide 46: Icing Forecasting System ExWx Provides Categorical Forecast of Icing
Predicting wind turbine icing is critical for power trading on open market and short term load balancing.
In order to successfully develop a robust wind turbine icing forecasting system, a truth dataset must be developed.
Limited documentation of icing events and monitoring equipment make identifying icing after the fact difficult.
Plus, there is a “Big Data” problem.

## Slide 47
WRF RTFDDA System
Natl Center Data
HRRR, NAM, GFS, RAP
GEM (Canada), ECMWF
Wind Farm Data
Nacelle wind speed
Generator power
Node power
Availability
VDRAS
(nowcasting)
Supplemental
Wind Farm Data
Met towers
Wind profiler
Surface Stations
Operator GUI
Meteorologist GUI
WRF Model Output
Wind to Energy Conversion Subsystem
Dynamic, Integrated Forecast System
(DICast®)
CSV Data
Statistical
Verification
Expert System
(nowcasting)
Ensemble System
Extreme Weather Events
Potential Power Forecasting
Data Mining for Load Estimation
Probabilistic and Analog Forecast
Solar Energy Forecast
Variable Energy Forecasting System

## Slide 48: Engineering the System
Big Data Application

## Slide 49
Wind Power Forecasts Resulted in Savings
for Ratepayers
Drake Bartlett, Xcel
Also: saved > 267,343 tons CO2 (2014)
  Forecasted MAE Percentage Savings
  2009 2014* Improvement
  16.83% 10.10% 40% $60,000,000
*Data through November, 2016
Notes: 2014 emissions savings for Colorado System (PSCo) due to economic cycling on baseload units = 267,343 tons of CO2. The ability to cycle baseload units (both coal and natural gas) is enhanced by confidence provided by accurate wind forecasting system

## Slide 50: Valuation
Production Cost Modeling
Accomplished by Utility Partner – Xcel
  Value of 50% Forecast Improvement: $820,000 (2024 – increased utility scale capacity)
Upscaled by NCAR (Lazo)
  Annual National Savings:
  $10 – $21M / year (2015-2024)
  26 year savings: $455M
Chart: Hour

## Slide 51
NWP Models
NAM
GFS
WRF-Solar
GEM
RAP/HRRR
Initial Grid
Interpolated to 4 km CONUS Grid
1-Hour Averaging
Archive data near observation sites
Observations
SMUD
MADIS
OK Mesonet
BNL
SURFRAD
Xcel
DeSota
ARM
Statistical Correction/Blending
DICast Point Correction
Gradient Boosted Regression Trees
Cubist
Random Forests
Analog Ensemble
Output Products
Maps of solar irradiance
Single point forecasts
% of clear sky irradiance
Future:
Other met. variables
Gridded Atmospheric Forecasts: GRAFS-Solar

## Slide 52: GRAFS
A new forecast is generated every hour
Individual images are generated for each lead-time
  Currently hourly out to 60 hours.

## Slide 53: GRAFS
AI methods at SMUD Sites

## Slide 54: Summary
Theme: Smartly blending data, dynamics, physics, and statistical learning methods
We need good models of the dynamics & physics
We need high quality data to assimilate
Statistical learning (artificial intelligence) can add value and help to determine the characteristics of the physics
Specialized applications may require specialized forecasts

## Slide 55
Questions

## Slide 56
Supplementary Slides

## Slide 57: StatCast
Forecast Clear Sky Index
Separate into:
  Clear
  Partly Cloudy
  Cloudy
Tyler McCandless

## Slide 58: Regime-Dependent Statcast
Tyler McCandless
Notes: The next step was to implement the Artificial Neural Network method for AI prediction. The predictors the model are provided include the past three GHI observations and the DICast predictors from all three sites for a total of 21 predictors. The data is split into a 2/3 training and 1/3 testing to optimally configure the model.

## Slide 59
Empirical Power Conversion Curves
Not Straightforward!
Manufacturer's Power Curve
Actual Power Curve
Gerry Wiener
Notes: 59

## Slide 60: Some Highlights
WRF-Solar improved on Standard WRF by 20-80%
WRF-Solar also important component of NowCast system, often best component
StatCast-Cubist can improve upon smart persistence by 37-62% - short range (0-3 hr)
TSICast better than persistence first 15 min – 29-34%
Cloud advection and assimilation methods predict ramps well – Nowcast with WRF-Solar-Now
Nowcast improvement 45-53% MAE averaged all conditions, all sites
Saw 47% improvement in prediction at Xcel sites, despite 2016 harder to predict (El Nino)
DICast® improves on best forecast
10-28% MAE
AnEn improves by another 16-96% MAE
SunCast improvement 90% MAE (SMUD)

## Slide 61: Recommendations for Solar Fcsting
Blend various component models or systems together with machine learning.
Use a base NWP model enhanced and tuned for the purpose.
Include multiple NWP models.
It is possible to improve upon persistence, even at the very short-range by using methods trained on in situ observations.
Satellite based cloud advection is useful, but tricky.
NWP can be combined with satellite data via assimilation for nowcasting.
The analog ensemble approach is helpful for both improving the deterministic blended forecast as well as for producing a probabilistic prediction.
An empirical power conversion method
viable, even where data limited.
Enhanced metrics necessary.